## Slide 1
Historical Meteorological High-Altitude Wind Diversity Analysis for Aerial Platforms
¹Distributed Autonomous Systems Group
Adaptive Systems Section (Code 5517)
U.S. Naval Research Laboratory
tristan.schuler@nrl.navy.mil
Tristan Schuler¹, Craig Motell²
HAWG
Dec 6, 2023
²???
???
Naval Information Warfare Center Hawaii
Craig.e.motell.civ@u.s..navy.mil
Notes: <number>

## Slide 2
Historical Wind Diversity Analysis | <number>
Introduction
Why is this historical wind analysis important?
Many High Altitude Platforms utilize or avoid certain winds for controllability in
  High Altitude balloons can use opposing and/or calm winds for station keeping and trajectory following
  Solar Planes look for calm or winds blowing in the path of flight to improve efficiency (is this true?)

## Slide 3
Historical Wind Diversity Analysis | <number>
Problems with using Global Forecasts for Wind Diveristy Analysis
Global forecasts are more sparse at higher altitudes. (Can be several km gaps in data)
  Comparing soundings to forecasts shows there is a lot of wind shifts in those gaps.
  QUESTION: Are there Global Forecasts (Gov or Public) with higher resolution?

## Slide 4
Historical Wind Diversity Analysis | <number>
Batch Analysis of Global Radiosonde Data
There are over 2000 weather stations across every continent that regularly launch radiosondes for assimilation into global forecast models
We are currently developing software to bulk download locally and perform batch analysis of global sounding data
Currently, we have downloaded and analyzed over 1.5 million soundings in North America for the past decade [2012-2023] to perform historical wind diversity analysis

## Slide 5
Historical Wind Diversity Analysis | <number>
How to Read a Traditional Wind Rose

## Slide 6
Historical Wind Diversity Analysis | <number>
Modifying Wind Roses (Going forward)
For data analysis we are changing from a traditional wind rose (BLOWING FROM) to a mathematical vector-based representation (BLOWING TO) for physics-based and numerical simulation
(BLOWING TO)
(BLOWING FROM)

## Slide 7
Historical Wind Diversity Analysis | <number>
3 Ways to visualize the same sounding
SPEED FREQUENCY
ALT FREQUENCY
“3D” POLAR WIND PLOT
[standard “blow to” wind rose]

## Slide 8
Historical Wind Diversity Analysis | <number>
Wind Diversity Analysis for HABs (15-25 km)
4 CATEGORIES for WIND DIVERSITY:
Fail, No Opposing winds
Calm winds (altitude region with winds <2 knots)
Opposing Winds (16-sector freq. analysis, at least 1 pair of opposing sectors)
Full Wind Diversity (8-sector freq. analysis, Either N-E-S-W or NE-SE-SW-NW)

## Slide 9
Historical Wind Diversity Analysis | <number>
Wind Diversity Analysis for HABs (15-25 km)
Fail, No Opposing winds
  Typical in the continental USA throughout the winter months (Nov-Mar) when the subtropical jet stream dominates
https://www.weather.gov/source/zhu/ZHU_Training_Page/winds/Wx_Terms/Flight_Environment.htm

## Slide 10
Historical Wind Diversity Analysis | <number>
Wind Diversity Analysis for HABs (15-25 km)
Calm winds (altitude region with winds <2 knots)
  QUESTION: What speed would you consider calm winds for aerial platforms

## Slide 11
Historical Wind Diversity Analysis | <number>
Wind Diversity Analysis for HABs (15-25 km)
Opposing Winds (16-sector freq. analysis, at least 1 pair of opposing sectors)
  QUESTION: Should there be additional parameters for labeling opposing winds?
  Could there be a scale/ranking of Opposing winds?

## Slide 12
Historical Wind Diversity Analysis | <number>
Wind Diversity Analysis for HABs (15-25 km)
Full Wind Diversity (8-sector freq. analysis, Either N-E-S-W or NE-SE-SW-NW)
  Not all full wind diversities are equivalent
  An ideal plot would have all sectors of equal size, and each one a different color)
Great full wind diversity
Poor full wind diversity
This small southerly wind sector at 21.5 km passes the full wind diversity test

## Slide 13
Historical Wind Diversity Analysis | <number>
Additional Obesevations
Diurnal Wind Changes
CRAIG, we need to change the location of this plot

## Slide 14
Historical Wind Diversity Analysis | <number>
Opposing Winds Monthly Probabilities
Altitude
Sounding Timestamp
Typically ~60 soundings per month per station
  More when tracking weather phenomenon (hurricane, cyclone, vortex, etc.)
Calculate the average probability at each altitude level in a given month

## Slide 15
Historical Wind Diversity Analysis | <number>
Opposing Wind Annual Probabilities
Salt Lake City (2022)
Corpus Christi (2014)
Boa Vista, Brazil (2021) [Near Equator]

## Slide 16
Historical Wind Diversity Analysis | <number>
North America Wind Diversity

## Slide 17
Historical Wind Diversity Analysis | <number>
Global Climatalogical effects Effects
El Nino, La Nina?
Coriolis Effects?
Climate Change
Hurricane Season,
Polar Vortex?
Etc.

## Slide 18
Questions?